## Slide 1: Diffusion Weighted MRS Numerical Simulation & Experimental Design for Microstructural Modeling
Marco Palombo, Ph.D.
Dep. of Computer Science and Centre for Medical Image Computing
University College London
UK
ISMRM Virtual Meeting: Diffusion Weighted MRS
9th August 2018

## Slide 2
Motivation for measuring the diffusion properties of brain metabolites
Tuning the DW-MRS experiment to measure cell morphology
Example 1: estimating cell morphology in vivo by DW-MRS
Example II: estimating brain cell fibres in vivo by DW-MRS
Example III: monitoring astrocytes reactivity in vivo by DW-MRS
Summary
Outline
ISMRM Virtual Meeting: Diffusion Weighted MRS
9th August 2018

## Slide 3
Non-invasive brain microstructure imaging by DW-MRI
Water diffusion-weighted MRI (DW-MRI) is a very powerful tool to characterize brain microstructure in vivo and non-invasively
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 4
Non-invasive brain microstructure imaging by DW-MRI
Water diffusion-weighted MRI (DW-MRI) is a very powerful tool to characterize brain microstructure in vivo and non-invasively
The patterns of diffusion displacement are sensitive to tissue microstructure
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 5
Water diffusion-weighted MRI (DW-MRI) is a very powerful tool to characterize brain microstructure in vivo and non-invasively
Tractography
DTI (Basser et al. 1994)
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Non-invasive brain microstructure imaging by DW-MRI

## Slide 6
Water diffusion-weighted MRI (DW-MRI) is a very powerful tool to characterize brain microstructure in vivo and non-invasively
NODDI (Zhang et al. 2012)
Orientation
Dispersion
Neurite
Density
CSF
Tractography
DTI (Basser et al. 1994)
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Non-invasive brain microstructure imaging by DW-MRI

## Slide 7
However brain tissue is very complex
Water is an aboundant but not specific probe of tissue microstructure
  Extra- and intra-cellular space
Different cell types
Complex medium (organelles and macromolecules)
  Exchange among compartments
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 8
Variations in cell morphology
Control
Alzheimer
20 µm
Neuron atrophy
Astrocyte reactivity
40 µm
Water: a not cell-specific probe of tissue microstructure
Water ADC
Water ADC
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 9
Brain metabolites are cell specific molecules
  Magnetic Resonance Spectroscopy (MRS) enables to quantify the concentration of brain metabolites
NAA – neuronal marker
tCr – energy metabolism
Glu, Gln – neurotransmitters
Cho, Ins – glial marker
GABA – neurotransmitter
Lac – anaerobic metabolism
Metabolites are mainly located in the intra-cellular space
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 10
DW-MRS is a unique tool to investigate the motion of brain metabolites in vivo.
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Brain metabolites are cell specific molecules

## Slide 11
DW-MRS is a unique tool to investigate the motion of brain metabolites in vivo.
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Brain metabolites are cell specific molecules
  Compartment specificity
  No extra-cellular space
[NAA] & [Glu], large consensus mostly in neurons
18 different studies suggest1
[Ins] in neurons (except NT2-N) < 4 mM
[Ins] in astrocytes ~ 12-15 mM
[Ins] ~ 3x higher in astrocytes compared to neurons
Fisher S et al., J Neurochem 2002
Urenjak J et al., J Neurosci. 1993
Le Belle JE et al. NMR Biomed. 2002
[tCho] ~ 2.5x higher in glia compared to neurons2
[tCho] ~ 10x higher in glia compared to neurons3
[tCho] ~ 6x higher in glia compared to neurons

## Slide 12
DW-MRS is a unique tool to investigate the motion of brain metabolites in vivo.
  Cellular morphology
  Cytosol viscosity
  Tortuosity
  Changes in intra-cellular structures
  Chemical reactions
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Brain metabolites are cell specific molecules
  Compartment specificity
  No extra-cellular space
Palombo M. et al. Neuroimage (2017)

## Slide 13
Variations in cell morphology
Control
Alzheimer
20 µm
Neuron atrophy
Astrocyte reactivity
40 µm
Cho
Ins
NAA
Glu
Metabolites: cell-specific probes of tissue microstructure
NAA ADC
Ins ADC
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 14
Brain intracellular metabolites mainly diffuse across length scales comparable with the whole cell structure1-5
We can use brain metabolites as probes of the brain cell morphology and intracellular space.
Marchadour C et al. Journal of Cerebral Blood Flow & Metabolism (2012)
Najac C et al. Neuroimage (2014)
Najac C et al. Brain Structure and Function (2014)
Ligneul C et al. Magnetic Resonance in Medicine (2017)
Palombo M. et al. Neuroimage (2017)
Diffusion weighted MRS can use metabolites as probe molecules
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 15
y
x
y
x
B(x)
x
B(x)
x
Homogeneous spatial distribution of Magnetic Field B
In-Homogeneous spatial distribution of Magnetic Field B
Magnetic Field Gradients to investigate molecular diffusion
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 16
Homogeneous spatial distribution of Magnetic Field B
In-Homogeneous spatial distribution of Magnetic Field B
y
x
y
x
B(x)
x
B(x)
x
B(a)
B(b)
a
b
B(a)
B(a)
B(a)
B(a)
B(a)
B(b)
B(b)
B(b)
B(b)
B(b)
B*
B*
B*
B*
B*
B*
B*
B*
B*
B*
B*
→ It is possible to induce specific magnetic field in-homogeneities to investigate probe molecules diffusion processes
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Magnetic Field Gradients to investigate molecular diffusion

## Slide 17
Homogeneous spatial distribution of Magnetic Field B
In-Homogeneous spatial distribution of Magnetic Field B
y
x
y
x
B(x)
x
B(x)
x
B(a)
x(ti) = a
B(b)
x(tf) = b
B(a)
B(a)
B(a)
B(a)
B(a)
B(b)
B(b)
B(b)
B(b)
B(b)
B*
B*
B*
B*
B*
B*
B*
B*
B*
B*
B*
→ In diffusion MR we use specific magnetic field gradient pulses to spatially label probe molecules and follow them during their diffusion process
DISPLACEMENT in time interval td=tf-ti
x(tf) – x(ti) = b-a
DISPLACEMENT in time interval td=tf-ti
??????
x(ti) = ???
x(tf) = ???
g≠0
g=0
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Magnetic Field Gradients to investigate molecular diffusion

## Slide 18
Homogeneous spatial distribution of Magnetic Field B
In-Homogeneous spatial distribution of Magnetic Field B
y
x
y
x
B(x)
x
B(x)
x
B(a)
x(ti) = a
B(b)
x(tf) = b
B*
B*
B*
B*
B*
B*
B*
B*
B*
B*
B*
→ strong g (short td) to be more sensitive to small molecules’ displacements
→ long td (weak g) to be more sensitive to large molecules’ displacements
DISPLACEMENT in time interval td=tf-ti
x(tf) – x(ti) = b-a
DISPLACEMENT in time interval td=tf-ti
??????
x(ti) = ???
x(tf) = ???
g
g*
g=0
B(a)
B(a)
B(a)
B(a)
B(a)
B(b)
B(b)
B(b)
B(b)
B(b)
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Magnetic Field Gradients to investigate molecular diffusion

## Slide 19
→ strong g (short td) to be more sensitive to small molecules’ displacements
→ long td (weak g) to be more sensitive to large molecules’ displacements
y
x
z
Short td
D0td < L2
Long td
D0td > L2
y
x
y
x
Weak g
qd < 1
Strong g
qd ≥ 1
L
d
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Magnetic Field Gradients to investigate molecular diffusion
q ~ Gradient Strength x Gradient Duration
d

## Slide 20
Intracellular viscosity
Fiber diameter (axons, dendrites…)
Organelles
Cell size
Long-range structural features
Diffusion time Td
0.1 ms
1 ms
10 ms
100 ms
1 000 ms
10 000 ms
Distance traveled Δx
0.3 µm
1 µm
2 µm
5 µm
15 µm
50 µm
Parameters affecting apparent diffusion
Molecular diffusion: a multi-scale approach
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 21
Intracellular viscosity
Fiber diameter (axons, dendrites…)
Organelles
Cell size
Long-range structural features
Diffusion time Td
0.1 ms
1 ms
10 ms
100 ms
1 000 ms
10 000 ms
Distance traveled Δx
0.3 µm
1 µm
2 µm
5 µm
15 µm
50 µm
Parameters affecting apparent diffusion
Short diffusion time: cytosol characteristics
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 22
Intracellular viscosity
Fiber diameter (axons, dendrites…)
Organelles
Cell size
Long-range structural features
Diffusion time Td
0.1 ms
1 ms
10 ms
100 ms
1 000 ms
10 000 ms
Distance traveled Δx
0.3 µm
1 µm
2 µm
5 µm
15 µm
50 µm
Parameters affecting apparent diffusion
Intermediate diffusion time: cell fibers and soma size
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 23
Intracellular viscosity
Fiber diameter (axons, dendrites…)
Organelles
Cell size
Long-range structural features
Diffusion time Td
0.1 ms
1 ms
10 ms
100 ms
1 000 ms
10 000 ms
Distance traveled Δx
0.3 µm
1 µm
2 µm
5 µm
15 µm
50 µm
Parameters affecting apparent diffusion
Long diffusion time: cell long-range morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 24
Long td (weak g)
→ Segments length
→ Number of consecutive bifurcation
× Segments and soma diameter
Tuning the DW-MRS experiment to measure cell morphology
long-range
cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 25
Strong g (short td)
× Segments length
× Number of consecutive bifurcation
→ Segments and soma diameter
Tuning the DW-MRS experiment to measure cell morphology
Long td (weak g)
→ Segments length
→ Number of consecutive bifurcation
× Segments and soma diameter
long-range
cell morphology
short-range
cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 26
Many possible sequences…but, which one to use?
Measuring molecular diffusion with DW-MRS
π/2
π/2
π/2
TE/2
TM
TE/2
echo
RF
Δ
δ
g
STEAM
Allows for long diffusion times keeping short the TE
Small chemical shift displacement
Advantages
Limitations
Strong cross-terms with background gradients
Loss of 50% of the signal
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Palombo M. et al. Neuroimage (2017)

## Slide 27
Many possible sequences…but, which one to use?
Measuring molecular diffusion with DW-MRS
Palombo M. et al. Neuroimage (2017)
π/2
π/2
π/2
TE/2
TM
TE/2
echo
RF
Δ
δ
g
STEAM
Allows for long diffusion times keeping short the TE
Small chemical shift displacement
Advantages
Limitations
Bipolar diffusion gradients  minimize eddy currents and background gradients
π/2
π
π
(TE1)/2
(TE2)/2
(TE1)/2
(TE2)/2
echo
RF
Δ
δ/2
g

PRESS
TE coupled to the diffusion times
Severe chemical shift displacement
Advantages
Limitations
Strong cross-terms with background gradients
Loss of 50% of the signal
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 28
Tuning the DW-MRS experiment to measure cell morphology
long-range
cell morphology
short-range
cell morphology
Long td (weak g)
→ Segments length
→ Number of consecutive bifurcation
× Segments and soma diameter
STEAM
Strong g (short td)
× Segments length
× Number of consecutive bifurcation
→ Segments and soma diameter
PRESS
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 29
→ b = q2 td ~ g2 δ2 td
Measuring molecular diffusion with DW-MRS
td≈60 ms
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
Diffusion Weighted NMR
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 30
→ b = q2 td ~ g2 δ2 td
td≈60 ms
NAA
Measuring molecular diffusion with DW-MRS
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
Diffusion Weighted NMR
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 31
→ b = q2 td ~ g2 δ2 td
→ S(b) = diffusion weighted signal attenuation
NAA
Measuring molecular diffusion with DW-MRS
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
Diffusion Weighted NMR
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
How to estimate microstructural features from DW-MRS data?

## Slide 32
→ ~106 spin trajectories & phases
Diffusion Weighted NMR
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
Simulating intra-cellular diffusion to characterize cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 33
→ ~106 spin trajectories & phases
→ S(b) ≈ exp[ -b ADC(td) ];
Diffusion Weighted NMR
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
Simulating intra-cellular diffusion to characterize cell morphology
Palombo M. et al. ArXiv preprint (2018) arXiv:1806.07125
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Numerical simulations can help us to identify the relevant microstructural features

## Slide 34
Tuning the DW-MRS experiment to measure cell morphology
long-range
cell morphology
short-range
cell morphology
Long td (weak g)
td ≳ 100 ms; b ≲ 5 ms/μm2
→ Segments length
→ Number of consecutive bifurcation
× Segments and soma diameter
STEAM
Strong g (short td)
td ≲ 80 ms; b >> 1 ms/μm2
× Segments length
× Number of consecutive bifurcation
→ Segments and soma diameter
PRESS
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 35
td ≳ 100 ms; b ≲ 5 ms/μm2
→ Segments length
→ Number of consecutive bifurcation
× Segments and soma diameter
Tuning the DW-MRS experiment to measure long-range cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 36
Astrocyte
Neuron
Dintra
Lsegment = 50  15 m
Nbranch = 2  2
5 model parameters
Dintra = effective medium diffusivity (organelles and macromolecular crowding, spines, cytoplasm viscosity, etc…)
Lsegment, Nbranch = long-range topological characteristics
SDLsegment, SDNbranch = metabolites compartments complexity and heterogeneity.
Palombo M. et al. PNAS (2016)
Statistical Model of brain cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 37
Lsegment = 75 µm
Lsegment = 50 µm
Lsegment = 25 µm
Effect of Lsegment (at constant Nbranch)
Palombo M. et al. PNAS (2016)
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 38
Nbranch = 1; Lsegment = 100 µm
Nbranch = 2; Lsegment = 50 µm
Nbranch = 4; Lsegment = 25 µm
Effect of Nbranch (at constant Nbranch x Lsegment)
Palombo M. et al. PNAS (2016)
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 39
Palombo M. et al. PNAS (2016)
Computational approach to estimate cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 40
Computational approach to estimate cell morphology
Parallel Tempering Initialization
+
Levenberg-Marquardt optimization
Accuracy ▲
Precision ▲
Stability ▲
Speed ▼
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Palombo M. et al. PNAS (2016)

## Slide 41
Computational approach to estimate cell morphology
Parallel Tempering Initialization
+
Levenberg-Marquardt optimization
Accuracy ▲
Precision ▲
Stability ▲
Speed ▼
Black box NOMAD
optimization
Accuracy ▲
Precision ▲
Stability ▼
Speed ▲
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Palombo M. et al. PNAS (2016)

## Slide 42
Computational approach to estimate cell morphology
Parallel Tempering Initialization
+
Levenberg-Marquardt optimization
Accuracy ▲
Precision ▲
Stability ▲
Speed ▼
Black box NOMAD
optimization
Accuracy ▲
Precision ▲
Stability ▼
Speed ▲
Machine Learning
Random Forest regressor
Accuracy ▲
Precision ▲
Stability ▲
Speed ▲
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Palombo M. et al. PNAS (2016)

## Slide 43
Macaque
Mouse
Neuronal overall diameter (~ 500 µm) agrees very well with typical extension of dendritic tree of many neurons
($) Oberheim N.A. et al. Journal of Neuroscience (2009) 29(10): 3276-3287
Overall astrocytes diameter 2.52 ± 0.10 times larger in macaque (2.55 ± 0.05 from histology$)
@ 7 T
@ 11.7 T
Interspecies Validation
Palombo M. et al. PNAS (2016)

## Slide 44
(GFAP staining)
(tCho and Ins)
Palombo M. et al. PNAS (2016)
Histological Validation

## Slide 45
(GFAP staining)
(tC ho and Ins)
Histological Validation
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Palombo M. et al. PNAS (2016)

## Slide 46
td ≲ 80 ms; b >> 1 ms/μm2
× Segments length
× Number of consecutive bifurcation
→ Segments and soma diameter
Tuning the DW-MRS experiment to measure short-range cell morphology
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 47
Palombo M. et al. MRM (2017)
A geometrical model for brain cell fibers
Diffusion Weighted NMR
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
In-vivo mouse at 11.7 T
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 48
Palombo M. et al. MRM (2017)
A geometrical model for brain cell fibers
0.62
Diffusion Weighted NMR
ECHO
/2
/2
/2
δ
δ
TM
τ
τ
g
td
Palombo M. et al. MRM (2017)
Burcaw L. et al. Neuroimage (2015)
DDE in-vivo rat (21.1 T)
NAA: a ≲ 0.75 μm
Myo-Inositol: 1.0 ≲ a ≲ 2.0 μm
Shemesh N. et al. PLOS One (2017)
PRESS in-vivo human (7 T)
NAA:
0.011 ≲ DT ≲ 0.025 μm2/ms
0.55 ≲ a ≲ 0.95 μm
Lundell H. et al. ISMRM (2017)
In-vivo mouse at 11.7 T
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 49
Astrocyte
‘Reactive’ Astrocyte
Injury and inflammation → Astrocytes reactivity
Why is the estimation of cell fibers size important?
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 50
Experiment 1: td ≲ 80 ms; b >> 1 ms/μm2 → Segments and soma diameter
20 µm
Astrocyte reactivity
Validation on mouse disease model : CNTF model
CNTF animal model of astrocytes activation
Ligneul C. et al. bioRxiv (2018)

## Slide 51
Experiment 2: td >> 10 ms; b ≲ 5 ms/μm2 → Segments length and branching
20 µm
Astrocyte reactivity
CNTF animal model of astrocytes activation
Ligneul C. et al. bioRxiv (2018)
Validation on mouse disease model : CNTF model

## Slide 52
Validation on mouse disease model: CNTF model
Quantifying astrocytes reactivity in vivo
Ligneul C. et al. bioRxiv (2018)
Ins
 |  | Lsegment (μm) | Variation (%) | Branch Order | Variation (%) | Dintra (μm2/ms) | Variation (%)
Histology | LacZ | 15 (±5) | +67 [***] | 6 (±4) | -33 [n.s.] | n.a. | n.a.
 | CNTF | 25 (±7) |  | 4 (±2) |  | n.a. | 
Synthetic (from Ins) | LacZ | 29 (±10) | +103 [***] | 6 (±5) | -17 [n.s.] | 0.376 (±0.008) | -2 [n.s.]
 | CNTF | 59 (±10) |  | 5 (±5) |  | 0.369 (±0.005) | 
 |  | Rsoma (μm) | Variation (%) | Rfiber (μm) | Variation (%) | Dintra (μm2/ms) | Variation (%)
Histology | LacZ | 3.7 (±1.2) | +29 [**] | 0.50 (±0.08) | +20 [**] | n.a. | n.a.
 | CNTF | 4.9 (±0.9) |  | 0.60 (±0.13) |  | n.a. | 
Synthetic (from Ins) | LacZ | 3.80 (±0.06) | +23 [***] | 0.58 (±0.02) | +47 [***] | 0.375 (±0.006) | -1 [n.s.]
 | CNTF | 4.66 (±0.07) |  | 0.85 (±0.02) |  | 0.372 (±0.005) | 

## Slide 53
Quantifying astrocytes reactivity in vivo
Ins
Ligneul C. et al. bioRxiv (2018)
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018
Validation on mouse disease model: CNTF model

## Slide 54
  DW-MRS provides unique microstructural information, complementary to DW-MRI
    Detect neuron-specific microstructural alterations (NAA, Glu).
    Detect glial-specific microstructural alterations (Ins, tCho).
    Investigate changes in energy metabolism related to neuronal activation (tCr).
  Experimental design is crucial: advanced numerical simulations help to identify the relevant microstructural features
  Data analysis is challenging: requires complex computational tools, appropriate biophysical modelling, histological reference
Summary
ISMRM Virtual Meeting: Diffusion Weighted MRS, 9th August 2018

## Slide 55: ESMRMB Lectures on MR: Diffusion weighted MRS
October 10-12, 2018 Paris/FR Course Venue ICM - Institut du Cerveau et de la Moelle épinière Hôpital Pitié-Salpêtrière Paris/FR
Course Organisers
Francesca Branzoli Center for neuroimaging research (CENIR) – ICM Paris/FR Itamar Ronen C.J. Gorter Center for High Field MRI Leiden University Medical Center Leiden/NL Julien Valette Molecular Imaging Research Center Commissariat à l'énergie atomique et aux énergies alternatives (CEA) Fontenay-aux-Roses/FR
ESMRMB Lectures on MR: Diffusion weighted MRS

## Slide 56
Acknowledgments
Thank you for your attention
MIG/CMIC, UCL, UK
Prof. Daniel Alexander
Dr. (Gary) Hui Zhang
ICM, France
Prof. Stephane Lehericy
Dr. Francesca Branzoli
INCELL project
MIRCen, CEA, France
Dr. Julien Valette
Dr. Edwin Hernandez-Garzon
Dr. Chloe Najac
Dr. Clemence Ligneul

## Slide 57: DW-MRS in cerebral ischemia
Understanding the mechanism of drop of water ADC in acute stroke.
The restriction in the extracellular space is not enough to explain the drop in ADC of water.
Some applications on Human

## Slide 58: Differentiating axonal and glial information with DW-MRS
I. Ronen et al, Front Integr Neurosci. 7:13, 2013
The ratio ADC(par)/ADC(perp) is consistent with the different compartmentalization of tNAA, tCr and tCho in axons and glial cells
  7 Tesla
  VOI = 15 x 8 x 25 mm3
Some applications on Human

## Slide 59: Microstructural organization of axons quantified by DW-MRS
Main eigenvectors ê1 overlaid on a FA map
(1,0,0)
θ1
g[1,0,0]
ê1
g[0,1,1]
θ2
θ1
θ2
I. Ronen et al, Brain Struct Func, 219,1773, 2013
tNAA
Distribution of the angles 1,2 between the main eigenvector ê1 and the two diffusion gradient directions g[0,1,1] and g[1,0,0].
Some applications on Human
Notes: Main eigenvectors e1 overlaid on a FA map

## Slide 60: Modeling DW-MRS data in the corpus callosum
Macroscopic curvature
∕ ∕
┴
+ Microscopic misalignment
θ1
(1,0,0)
ê1
θ1
(1,0,0)
ê1
Histologic image and FODs
  18°
Dmodel(tNAA)  0.51
I Ronen et al, Brain Struct Func, 219,1773, 2013; P van Gelderen et al, J Magn Reson B, 103,255, 1994.
Model of diffusion in parallel cylinders, including macroscopic axonal dispersion and microscopic misalignment.
Some applications on Human

## Slide 61: Reproducibility and optimization of DW-MRS data at 3T and 7T
Inter- and intra-subject variability
Optimized acquisition scheme of 13 minutes at 3T
Power calculation for clinical studies
E Ercan et al, NMR Biomed, 28, 976, 2015
Some applications on Human

## Slide 62: tNAA diffusion in healthy aging
  Subjects: 13 healthy elderly subjects (64 ± 3 yrs), 17 young controls (27 ± 5 yrs).
  Scanner: Philips 7T whole body, Volume Tx/32ch Rx.
  DW-MRS: - VOI 2.5cm (AP) x 1.5 cm (RL) x 0.8 cm (FH), 32 averages,
        - PRESS sequence, TE/TR= 121ms/3 cardiac cycles,
        - b = 600, 1920, 3800, 6200 s/mm2 (radial direction),
        - b = 330, 960,1900, 3100 s/mm2 (axial direction).
        - Scan time = 15 min.
F Branzoli et al, submitted to Neurobiol Aging
  3D T1-weighted, DTI sequence
  MRI/MRS protocol
Some applications on Human

## Slide 63: Differentiating between axonal damage and demyelination in healthy aging
FA
MD
RD
The intra-axonal damage in healthy elderly in this age range is negligible or even absent
Do water AD changes reflect intra-axonal damage?
tNAA | Young | Elderly | P value
Dmodel(μm2/ms) | 0.53 ± 0.04 | 0.51 ± 0.04 | 0.21
D//(μm2/ms) | 0.39 ± 0.04 | 0.37 ± 0.03 | 0.12
D┴ (μm2/ms) | 0.08 ± 0.01 | 0.08 ± 0.02 | 0.79
σφ (deg) | 12 ± 5 | 12 ± 5 | 0.77
TBSS analysis
DW-MRS
The differences in water FA, MD and RD are consistent with the onset of demyelination processes
decrease
increase
F Branzoli et al, submitted to Neurobiol Aging
Some applications on Human

## Slide 64
Diffusion tensor spectroscopy in multiple sclerosis
ET Wood et al, J Neurosci, 32(19) 6665, (2012).
  NAA axial diffusivity decrease possibly reflects an early neuroaxonal damage.
  Water axial diffusivity cannot be used as a marker for intra axonal damage, since it is also susceptible to demyelination.
 Presentation of Benedetta Bodini, today at 14:30
Some applications on Human

## Slide 65: Glial and axonal changes in SLE measured with metabolite diffusion
E Ercan et al, Brain, 2016
  Subjects: 29 patients with SLE (19 with NPSLE), 19 age- and sex-matched controls.
  Scanner: Philips 7T whole body, Volume Tx/32ch Rx.
  3D T1-weighted, DTI sequence
  MRI/MRS protocol
  DW-MRS
  Systemic lupus erythematosus (SLE) is an inflammatory autoimmune disease with multi-organ involvement.
Some applications on Human
Notes: In this study diffusion tensor imaging and diffusion spectroscopy were combined in order to investigate cell-specific microstructural changes in patients with SLE and neuro-psychiatric SLE.

## Slide 66: Glial and axonal changes in SLE measured with metabolite diffusion
FA
MD
RD
decrease
increase
E Ercan et al, Brain, 2016
  Diffusion of tCho and tCr are potentially unique markers of glial reactivity in response to inflammation.
Some applications on Human

## Slide 67: Functional DW-MRS
= non diffusion weighted (b~0 s/mm2)
= diffusion weighted (b~4000 s/mm2)
  Investigate compartment-specific microstructural and/or metabolic changes related to neuronal activation.
  Direct detection of neuronal activation by measuring metabolite diffusion during visual stimulation.
×24
Functional paradigm
24 blocks of 32 scans each:
- 2x8 scans rest period
- 2x8 scans of activation.
F. Branzoli et al, MRM, 69:303–309 (2013)
  Subjects: 14 healthy volunteers.
  Scanner: Philips 7T whole body, Volume Tx/32ch Rx.
Some applications on Human

## Slide 68
Increase of tCr diffusion during neuronal activation
Cell swelling (D Le Bihan et al, PNAS, 2006)
p = 0.002
p = 0.05
p = 0.03
Decrease in PCr/Cr ratio
(W. Chen et al. MRM 38 551- 557 (1997). H. Lei et al. Proc. Intl. MRM, p 11, 2004. S. Xu et al., NeuroImage, 28, 401 – 409 2005)
 Increase of Creatine Kinase activity
PCr + ADP + H+ ↔ Cr + ATP
F. Branzoli et al, MRM, 69:303–309 (2013)
  tCr , tNAA, tCho diffusion coefficient increase during visual stimulation.
Some applications on Human

## Slide 69
Diffusion-weighted chemical shift imaging of brain metabolites
Ercan E et al, Magn Res Med, 2015
  Real-time navigator-based acquisition scheme.
  Instantaneous reacquisition of corrupted k-space data.
  Correction of gradient induced phase fluctuations.
Some applications on Human
Notes: only a few attempts have been made so far at obtaining maps of the diffusion properties of brain metabolites with DW-CSI
The long scanning times these experiments require limit their clinical
applicability, and so far they have been characterized by a lack of robustness and reproducibility.
The phase encoding gradient is placed after the second lobe of the refocusing diffusion gradient and before the echo
maximum such that 25–30 navigator data points are acquired
prior to the phase-encoding step. A turbo spectroscopic imaging
mode with two echo acquisitions (TE¼100/205 ms)
was used, and 256 sample points were acquired for each
of the two echoes with a spectral bandwidth of 5000 Hz. This threshold was then used in
real-time as an accept/reject criterion for subsequent
acquisitions for that diffusion condition such that for
each k-space location, data that fell below the threshold
were reacquired. An upper limit for the number of reacquisitions
was set to 100 for each diffusion condition.
The navigator time-domain data were zero-filled to 128
points and line-broadened. Following a Fourier transformation,
a coarse spectrum of the navigator was obtained.
The phase for each acquisition was then estimated
from the residual water, and diffusion-induced phase
fluctuations were removed using the formula…

## Slide 70
Diffusion-weighted chemical shift imaging of brain metabolites
  The metabolite ADC values could be related to the underlying tissue composition.
Ercan E et al, Magn Res Med, 2015
Some applications on Human
Notes: Metabolite ADC values obtained in this study related meaningfully to the underlying tissue cellular composition